State of Charge Monitor

Use temperature, voltage and bi-polar current measurements with a programmable logic controler to reliably monitor the state of charge of a domestic LifeP04 battery bank that is charged by various sources.

Dave Gutz January 12, 2023 first draft

# Abstract:
Users of the latest, efficient rechargeable battery banks need to know how much charge remains. This becomes important for estimating the range of travel for an electric car, for example – the 'gas gauge replacement.' In my case, when truck camping with my CPAP machine I need to know if there is enough charge in the RV battery bank to power the CPAP overnight. I've never woke up gasping and I want to minimize that possibility. Old technology batteries, e.g. Lead-acid, have a steep curve relationship between terminal voltage and state-of-charge (SOC). This makes it easy to use a voltmeter as a capacity gage. The flat voltage-SOC characteristic of modern LiFeP04 batteries – safe to install in sleeping quarters and efficient charge handlers – makes it nearly impossible to guess SOC from voltage measurement. Further complicating the task, the electrical hysteresis where voltage depends on direction of charging/discharging and time history is large compared to the SOC characteristic. Hysteresis uncertainty approaches the entire SOC curve from fully discharged to fully charged. A 'smart,' reliable monitor is needed. Smart would be capabilities that keep track of the time history to as accurately as possible predict time remaining for current usage. Reliable would be features that keep the system operational in the presence of common failures, allowing the user to repair the system at their convenience with no downtime. At present, my system is designed for a couple, one-off prototypes and relies on calibration of inexpensive components for precision. The known condition of full saturation is easily detected and used to re-calibrate the device on the fly. Hardware RC filtering is needed to cleanup the sensor signals from noise injected by AC inverter devices. A 1 Hz low-pass filter is all that is needed. Since SOC is a long term, e.g. 24 hour integration process – a very slow low-pass filter in itself, no precision is lost using the hardware RC filtering. Therefore advanced software filtering is not required for the main task of counting Coulomb charge. An Extended Kalman Filter (EKF) advanced filtering is useful, however, to detect component failures and establish reliability. I used Mathworks' EKF prototype. I created my own 'reservoir' charge model to track hysteresis. I found that reasonable reliability is achieved with simplex temperature sensing, simplex voltage sensing, and dual current sensing. The combination of two current signals, one voltage sensor, the EKF, and known SOC characteristic (voltage-currrent-time history) enables the equivalent of triplex current sensing. Quiet signal detection logic detects that a current sensor is disconnected either by wiring or failure to help isolate. The 1-wire temperature sensor and the mini-OLED display are replaceable. Faults and history are recorded in EERAM for later retrieval. A standalone Python data reduction program (DRP) allows comparing history with a model to understand operation. The DRP also serves as regression machine to compare software changes with past changes, to develop component maps for characterizing a system, and to investigate problems. Some learnings: The system needs to run at about 0.1 seconds update to accurately capture by integration the peaks and valleys of battery bank usage. The EKF needs to run double precision and slower update rate, about 0.5 seconds, to handle the numerics of the system. It is possible to self-calibrate by comparing total charge history to total discharge history between known charge states – full charge. By triangulation of data history, the charging efficiency of the batteries needs to be estimated to complement the history data. System uncertainty for this home-made system is large so that this self-calibration adds no value and was deleted. Simple scalar-adder calibration of the installed current sensor using a clamping current meter is sufficient to establish monitor precision within about a half hour of time remaining estimate. The system needs to be intentionally discharged and recharged at expected operating temperatures to characterize the SOC-voltage map and hysteresis model. Triangulation of data, i.e. repeated calibration runs from full charge to full discharge, allows estimation of the battery capacity versus rated while calibrating the current sensors (full charge condition is repeatable). Battery life may be monitored by repeat calibration. Most of my findings are preliminary based on my observations of prototypes and a lot of experience in the developement of computer controlled systems. I took advantage of my 'skunk works' arrangement in retirement. Rigorous study is needed to establish the findings as fact for some product device.

Figure 1: State of Charge Wiring Diagram Board Layout
## Battery Unit
For convenience all modeling is done in relation to a 12v battery of a certain manufacturer. The user specifies the rated capacity. The user has to develop, beg, borrow, and steal these characteristics and ultimately test their own battery through a full discharge/charge cycle. But once this is set, battery banks are built by scaling the number of series and parallel units, (nS and nP). Those numbers are floating point for maximum flexibility. A 2S3P bank would consist of 4 batteries. The voltage output would be 2x a unit (24v) and the current output would be 3x a unit. This scaling may be done at the sensor interface and at the display interface. Then the computations – modeling and counting are done with the single battery unit.

## Caution
The voltage sensor is a 3.3v A/D on the PLC to measure 15v. Exceeding 3.3v will blow the A/D and make the monitor mostly useless. It would be difficult to know saturation, a critical sensing element for basic accuracy. A voltage divider is soldered to do this. If more batteries are added in series, then the low voltage leg of the divider will need less resistance. See the 4k7 resistor on the right hand side of the main board diagram at top – feeding A1. It's easy to add a parallel resistor to achieve this whereas the high voltage leg would require removing solder. There is a way to add this resistor to the back of the main PLC board accessed by removing the cover of the device. Remember to rescale and recalibrate the voltage measurement in the monitor application.

## Current Sensor Design
Shunt return a small voltage for a current passing through it. The voltage is small to avoid affecting system performance and generating heat. The voltage is biploar because current may either charge or discharge. So an amplifier is required to generate a high voltage for a 3.3v unipolar A/D that does not change sign. This is easy to do with a single op-amp. See Figure 2. For a shunt that puts out 0.075v at rated current a gain of about 20 is needed. The RC filtering (R1*C106) is performed on the output to also serve as anti-aliasing of op-amp and other circuit noise.

A disadvantage of this design is that 4 A/D are needed for two sensors. Each sensor needs the output voltage and also the common voltage. There is a chip available, TSC2010-IDT, that does differential amplification using three built-in op-amps. The base chip is TSC201. The trailing "0" denotes 20 amplification. There are others: the next size up, "1" is 60. The IDT is the standard quality control for an SOIC-8 surface mount. These sensors use high quality internal resistors and cost about $5.00 each but were not available until 6 months after building the Beta prototype.

## Repository
All information including code, data sheets, scripts, the source for this document is organized in the open GitHub repository https://github.com/davegutz/myStateOfCharge. The MIT license is applied to make all this information open.
Most information is in the primary application folder SOC_Photon, named after the first prototype: a Particle Photon PLC running a 'state of charge' counting algorithm.
Moving alphabetically, the first folder 'Battery State' is a record regarding the theory of LiFeP04 battery state of charge (SOC) monitoring. The subfolder 'EKF' is a record of theory of Extended Kalman Filter as applied to SOC. Inside the 'sandbox' folder are Python models of this topic.
The second folder 'dataReduction' collects raw CoolTerm data capture files '.txt.' The README.md file at the top level has a listing of the different types of scripts run using the 'talk' function through CoolTerm UART transmit/receive interface to generate these files. That is normally done as regression testing to understand code change. Those are sometimes renamed as '.xls', '.xlsx', or '.ods' to plot by hand using Microsoft Excel or Open Document Spreadsheet. By renaming them the hand work is remembered in the repository and not over-written by the next regression test runs through the script series. The '.stc' files are CoolTerm configuration files that are useful to save. The subfolder 'figures' is a permanent collection of data reduction runs, see the 'py' folder of the data reduction Python scripts. The subfolder 'temp' is a scratch folder used by the Python scripts. The '.csv' files in there are useful for debugging the Python scripts.
The folder 'datasheets' has hardware datasheets as well as snapshots of any hand-drawn schematics in 'Schematics' and a folder 'pSpice' with Ltspice modeling of the circuits.
The folder 'lib' is created by VisualStudio Particle Workbench to import Particle-specific code libraries.
The folder 'py' was mentioned before. It is the Python scripts used for data reduction. It was handy to run the same scripts to overlay data on predicted model results. So any design work could be performed by iterating on a particular script run that has a problem, modifying the Python model of the application to find solutions. Inside 'py' is a folder 'pyDAGx' where I store my own Python libraries. The 'venv' folder is maintained by pyCharm IDE.
The folder 'src' has the application source. The app is 'SOC_Photon.ino.' Particle follows the Arduino naming convention. The '.sav' files are my record of a concept that 'tweaked' the charging efficiency to match Coulomb Counting history to incidence of saturation. The concept assumes the current sensors are calibrated perfectly. Inside this folder are 'Adafruit' libraries imported by hand instead of the Particle process, 'hardware' libraries for miscellaneous devices, and 'myLibrary' with my stuff I've accumulated over time – mainly dynamic filters used for application logic.
The folder 'target' is generated by the Particle Workbench to hold application .elf files.

There is a gsheet at https://docs.google.com/spreadsheets/d/19PZ2GmKIlw14doqwePp9xxWH96coLm8WmXdIwlzdxjE/edit#gid=167481175 called 'Truck Camping ALL STUFF' that has a minifest of the prototype hardware. See the tabs 'SOC Device Alpha' and 'SOC Device Beta.' Alpha refers to the Photon design with ADS cards feeding I2C. Beta refers to the Argon design with pure OpAmp devices.
## Design Process Philosopy
For this project I followed a streamlined method that I hope 'self documents.' Data reduction centers on an 'overplot' idea. The run regression, I would overplot the result of old runs on new runs looking for and verifying differences. To run verification, I would overplot the result of new runs on the new model, looking for differences. In verification, there should be a perfect overplot. There are some very rare instances where the data does not overlay perfectly. The presumption is that in achieving a perfect overlay that design meets intent and I avoided a painfully detailed explanation of plot artifacts. Design documentation is done at a higher level with a rough description, not too much detail that would detract from understanding.

## Prototypes
Two situations drove the prototypes and sometimes choice of design.

First, sampling of a low-voltage bipolar current shunt is a the most challenging hardware design in this project. At first I tried to leverage a device described in the literature. It sampled the low voltage using the differential inputs into an A/D converter (ADS1013) sent along an I2C to the Particle devices. It was later improved by adding an op-amp (OPA333) as suggested by Texas Instruments engineers in the datasheets for the ADS1013. This got me started and lives on in the Photon prototypes. Eventually I realized that the Particle devices have plenty of A/D converters and that the real challenge was to make a high accuracy bipolar instrumentation amplifier. The biggest problem with the ADS I2C solution is the throughput. Every call to the I2C device uses between 1 and 100 ms of dead wait time. This sets the throughput for the application. To capture current spikes properly a 0.100 second (100 ms) update time is needed. The Particle A/D converters us micro second range read times. There is a 20:1 chip that matches the 3.3v and 0.075v ranges of the Particle A/D and shunt output range made by ST Microelectronics called TSC2010-IDT that is perfect for the task and costs less that $4. It was not available due to COVID pandemic shortatges so instead I used two one-sided A/D converters to manage primary and common voltages of the one-sided OPA333 op-amp circuits to calculate sensed current. This is less accurate but workable since there is plenty of A/D interfaces.

Second, Particle devices are morphing over time. The Photon is their first / second generation device with Wifi interface and built-in EEPROM to handle power loss. I interfaced to TX/RX UART an HC-06 standard Bluetooth (as opposed to the newer low-energy BLE) for monitoring by the user while moving. When those ran out Particle offers up the third-generation Argon also with Wifi that does not have built-in EEPROM but does have built-in BLE. I bought 47L16 EERAM I2C modules to replace the EEPROM function. This required considerable application programming to support. I tried the BLE function but found that UART terminal apps to support it are poor. So I continued on with the HC-06 since it was a ready solution. The future of Particle is the Photon 2. I would recommend the Photon 2 Development Kit. They are not yet available. It will require the EERAM and HC-06, most likely, unless UART BLE terminals magically appear.

An almost third situtation was software morphing. Particle requires software versions to match hardware devices and those change over time. Fortunately this application is simple enough that basic firmware could handle it and firmware bugs did not affect it. I simply kept up with Particle's releases, always using the most recent as they came out.
## Relibility Concept
Triplex
Identify annunciate problems so they are fixed, to maintain availabilty
Power loss
Fault buffers
Temp
## Real-Time Monitoring
There are three possible ways:
- Connect CoolTerm to the USB
- Connect phone UART terminal to the USB
- Monitor HC-06 standard Bluetooth Serial Output
## Post Process Monitoring
High sample rate is needed to properly bookkeep current integration for spikes. Once that is verified and built in the device build the monitoring process may have as long as 30 minutes between data points. Sensor failures are on the order of 10 seconds between data points. Two circular buffers manage this data collection. Seven points are captured for any critical sensor failure and that buffer frozen until manually reset. It may be downloaded using any of the three monitoring methods. Any and all excess memory is used for the history. The Argon PLCs have some extra EERAM beyond what's needed for sensor failures. And the Argon PLCs have extra PRAM to access as long as the PLC is not depowered. All these are available using any of the three monitoring methods.
## Resistor Quality
The temperature range for this device is about 0C for a heated battery up to about 40C on hot summer day. This is a small swing and 5% resistors would show about 1% effect. And since the battery hysteresis, variation, life and the need to calibrate for installation effects drive accuracy, the resistor quality could be poor. This is unnecessary because the high quality resistors are negligibly more expensive. In the future, 1% 1/4 watt resistors should be procured.

## Cost

## Battery Heating

Figure 2: Current Sensors Functional Circuit Diagram
# Recommendations
1. Procure TSC2010-IDT chips going forward.
2. Procure 1% 1/4 watt resistors going forward.