State of Charge Monitor

Use temperature, voltage and bi-polar current measurements with a programmable logic controler to reliably monitor the state of charge of a domestic LifeP04 battery bank that is charged by various sources.

Dave Gutz January 12, 2023 first draft

# Abstract:
Users of rechargeable battery banks need to know how much charge remains. This becomes important for estimating the range of travel for an electric car, for example – the 'gas gauge replacement.' In my case, when truck camping with my CPAP machine I need to know if there is enough charge in the RV battery bank to power the CPAP overnight. I've never woke up gasping and I want to minimize that possibility. Old technology batteries, e.g. Lead-acid, have a steep curve relationship between terminal voltage and state-of-charge (SOC). This makes it easy to use a voltmeter as a SOC gage. Newer batteries developed for electric cars are different. The flat voltage-SOC characteristic of modern LiFeP04 batteries – safe to install in sleeping quarters and efficient charge handlers – makes it nearly impossible to guess SOC from voltage measurement. Further complicating the task, the electrical hysteresis where voltage depends on direction of charging/discharging and time history is large compared to the SOC characteristic. Hysteresis uncertainty approaches the entire SOC curve from fully discharged to fully charged. A 'smart,' reliable monitor is needed. Smart would be capabilities that keep track of the time history to as accurately as possible predict time remaining for current usage. Reliable would be features that keep the system operational in the presence of common failures, allowing the user to repair the system at their convenience with no downtime. At present, my system is designed for a couple, one-off prototypes and relies on calibration of inexpensive components for precision. The known condition of full saturation is easily detected and used to re-calibrate the device on the fly. Hardware RC filtering is needed to cleanup the sensor signals from noise injected by AC inverter devices. A 1 Hz low-pass anti-alias filter in hardware is all that is needed. Since SOC is a long term, e.g. 24 hour integration process – a very slow low-pass filter in itself, no precision is lost using the hardware RC filtering. Therefore advanced software filtering is not required for the main task of counting Coulomb charge. An Extended Kalman Filter (EKF) advanced filtering is useful, however, to detect component failures and establish reliability. I used Mathworks' EKF prototype. I created my own 'reservoir' charge model to track hysteresis. I found that reasonable reliability is achieved with simplex temperature sensing, simplex voltage sensing, and dual current sensing. The combination of two current signals, one voltage sensor, the EKF, and known SOC characteristic (voltage-currrent-time history) enables the equivalent of triplex current sensing. Quiet signal detection logic detects that a current sensor is disconnected either by wiring or failure to help isolate. For strictly hardware reliability reasons, the 1-wire temperature sensor and the mini-OLED display are line replaceable. Faults and history are recorded in EERAM for later retrieval. A standalone Python data reduction program (DRP) allows comparing history with a model to understand operation. The DRP also serves as regression machine to compare software changes with past changes, to develop component maps for characterizing a system, and to investigate problems. Some learnings: The system needs to run at about 0.1 seconds update to accurately capture by integration the peaks and valleys of battery bank usage. The EKF needs to run double precision as well as slower update rate, about 0.5 seconds, to handle the numerics of the system. It is possible to self-calibrate by comparing total charge history to total discharge history between known charge states – full charge. By triangulation of data history, the charging efficiency of the batteries needs to be estimated to complement the history data. System uncertainty for this home-made system is large so that this self-calibration adds no value and was omitted from the published version. Simple scalar-adder calibration of the installed current sensor using a clamping current meter is sufficient to establish monitor precision within about a half hour of time remaining estimate. To calibrate the system, the user needs to be intentionally discharged and recharged at expected operating temperatures to characterize the SOC-voltage map and hysteresis model. Triangulation of data, i.e. repeated calibration runs from full charge to full discharge, allows estimation of the battery capacity versus rated while calibrating the current sensors (full charge condition is repeatable). In the case of a CPAP system, I used a couple household fans to simulate actual load and ran data collection overnight in the driveway with the fans while I slept in the house with my CPAP. Battery life may be monitored by repeat calibration. Most of my findings are preliminary based on my observations of prototypes and a lot of experience in the developement of computer controlled systems. I took advantage of my 'skunk works' arrangement in retirement. Rigorous study is needed to establish the findings as fact for some product device.

## Off-the-Shelf Hardware Description
I used prototype boards to connect various off-the-shelf devices into a reliable, maintainable box. The heart of the system is the Particle programmable logic controller (PLC). I've incorporated both the Photon gen 1 device and the Argon gen 3 device. Figure 1 shows the latest Argon schematic. The Photon is no longer available. The Argon will disappear soon too probably in 2023. The recommended replacement is Photon 2. I suggest getting the developer kit that has headers and other peripherals such as USB installed.

The 47L16 EERAM device provides memory to the Argon through power loss, sometimes caused by the battery management system (BMS) of the battery itself as well as user events.

OPA333 op-amp circuits, two for reliability, convert the biploar +/- 0.075 volt Bayite shunt signal, current range 100 Amps, into full range 0-3.3v A/D signal. The current signal uses a dedicated, shielded sense line to feed high impedance op-amp cicuites to avoid line effects.

A voltage divider circuit measures battery voltage straight from the device power supply. Caution: the Particle devices blow if A/D voltage exceeds 3.3v. If the prototype is used on a two-battery series 2S system, the voltage divider circuit needs modification.

A 12v – 5v converter circuit feeds power to the Particle device and the 1-wire temperature sensor. The Particle device in turn converts 3.3 v for other devices – op-amp, EERAM and OLED display. The Particle device also has a USB. The power demands do not exceed the capacity of the Particle so USB only usage is possible for user off-line testing. Measurement of 12v supply is missing in this mode.

All the hardware if the least expensive possible. Battery uncertainty drives accuracy. And low rate of production make use of user calibration feasible.

The initial battery used to test the system, and use on RV trips, was the Battleborn 100 A-h LiFeP04. It is the most expensive battery available and comes with an industry-leading BMS that prevents damage from misuse. I thought that was important for the first prototype. Chins batteries are available at 1/3 the price.

Figure 1: State of Charge Wiring Diagram Board Layout
## Requirements
 1. Calculate state of charge of 100 Ah Battleborn LiFePO4 battery. The state of charge is percentage of 100 Ah available.
  a. Nominally the battery may have more than 100 Ah capacity. This should be confirmed.
  b. Displayed SOC may exceed 100 but should not go below 0.
 2. Displayed values when sitting either charging slightly or discharging DC ciruits (no inverter) should appear constant after filter rise.
  a. Estimate and display hours to 1 soc. (charge is positive). This is the main use of this device: to assure sleeper that CPAP, once turned on, will last longer than expected sleep time.
  b. Measure and display shunt current (charge is positive), A.
  c. Measure and display battery voltage, V.
  d. Measure and display battery temperature, F.
 3. Implement an adjustment 'talk' function. Along with general debugging it must be capable of
  a. Setting soc state
  b. Separately setting the model state
  c. Resetting pretty much anything
  d. Injecting test signals
 4. CPU hard and soft resets must not change the state of operation, either soc, display, or serial bus.
 5. Serial streams shall have an absolute Julien-type time for easy plotting and comparison.
 6. Built-in test function, engaged using 'talk' function.
 7. Load software using USB. Wifi to truck or phone (hotspot) may not be reliable. Related requirement: provide holes to press Particle Device buttons: sometimes setup long-press needed or manual flash request needed with these devices.
 8. Likewise, monitor USB using laptop or phone. 'Talk' function should change serial monitor and inject signals for debugging.
 9. Device shall have no effect on system operation. Monitor function only.
 10. Bluetooth serial interface required. ***This did not work due to age of Android phone (6 yrs) not compatible with the latest bluetooth devices.
 11. Keep as much summary as possible of soc every half hour: Tbatt, Vbatt, soc. Save as SRAM battery backup memory. Print out to serial automatically on boot and as requested by 'Talk.' This will tell users charging history.
 12. Adjustments to model using talk function should preserve delta_q between models to preserve change from
 saturated situation. The one 'constant' in this device is that it may be reset to reality whenever fully
 charged. Test it the same way. The will be separate adjustment to bias the model away from this ('n' and 'W')
 13. The 'Talk' function should let the user test a lot of stuff. The biggest short coming is that it is a little quirky. For example, resetting the Photon or doing any number of things sometimes requires the filters to be initialized differently, e.g. initialize to input rather than tending toward initializing to 0. The initialization was optimized for installed use. So the user needs to get used to rationalizing the initialization behavior they see when testing. They can wait for the system to settle, sometimes 5 minutes. They can run Talk('Rs') to attempt a software filter reset - won't help if the test draws a steady current after reset/reboot.
 14. Inject hardware current signal for testing purposes. This may be implemented by reconnecting the shunt input wires to a PWM signal from the Photon.
 15. The PWM signal for injecting test signals should run at 60 Hz to better mimic the 60 Hz behavior of the inverter when installed and test the hardware AAF filters, (RC=2*pi, 1 Hz -3dB bandwidth).
 16. There shall be a built-in model to test logic and perform regression tests. The EKF in MyBatt needs a realistic response on current to voltage to work properly (H and hx assume a system). The built-in model must properly represent behavior onto and off of limits of saturation and 0.
 17. The Battery Monitor will not properly predict saturation and low shutoff. It doesn't need to. The prime requirement is to count Coulombs and reset the counter when saturated. The detection of saturation may be crude but always work - this will result in saturation being declared at too low voltage which is conservative, in that the logic will display a state of charge that is lower than actual.
 18. The Battery Model used for testing shall implement a current cutback as saturation is neared, to rougly model the BMS in the actual system.
 19. The Battery Monitor shall implement a predicted loss of capacity with temperature. The Battery Model does not need to implement this but should anyway.
 20. The Battery Model shall be scaleable using Talk for capacity. The Battery Monitor will have a nominal size and it is ok to recompile for different sizes.
 21. The Battery Model Coulomb Counting algorithm shall be implemented with separate logic to avoid the problem of logic changes confounding regression test.
 22. The Talk function shall have a method Talk('RR') that resets all logic to installed configuration.
 23. The default values of sensor signal biases should remain as default values in logic.
 24. Power loss and resets (both hard and soft) must not affect long term Coulomb counting. This may result in adding a button-cell battery to the VBAT terminal of Photon and using 'retained' SRAM data for critical states in the logic. It would be nice if loss and resets did not affect Battery Model and testing too.
 25. 'soc' shall be current charge 'q' divided by current capacity 'q_capacity' that reflects changes with temperature.
 26. Coulomb counting shall simultaneously track temperature changes to keep aligned with capacity estimates.
 27. 'SOC' shall be current charge 'q' at the instant temperature divided by rated capacity at rated temperature.
 28. The monitor logic must detect and be benign that the DC-DC charger has come on setting Vb while the BMS in the battery has shutoff current. This is to prevent falsely declaring saturation from DC-DC charger on.
 29. Only Battleborn will be implemented at first but structure will support other suppliers. For now, recompilation is needed to run another supplier and #define switches between them.
 30. The nominal unit of configuration shall be a 12 v battery with a characteristic soc-voc and rated Ah capacity. Use with multiple batteries shall include running an arbitrary number of batteries in parallel and then series (nPmS). The configuration shall be in local_config.h and in retained.h. This is called the 'chemistry' of the configuration.
 31. The configuration shall be fully adjustable on the fly using Talk. If somebody has Battleborn or a LION they will not need to ever recompile and reflash a Photon.
 32. Maximize system availability in presence of loss of sensor signals. Soft or hard resets cause signal fault detection and selection to reset. Flash display to communicate signal status: every fourth update of screen indicates a minor fault. Every other update is major fault where action needed. Print signal faults in the 'Q' talk. Add ability to mask faults to a retained parameter rp.

## Battery Unit Concept
For convenience all modeling is done in relation to a 12v battery of a certain manufacturer. The user specifies the rated capacity. The user has to develop, beg, borrow, and steal these characteristics and ultimately test their own battery through a full discharge/charge cycle. But once this is set, battery banks are built by scaling the number of series and parallel units, (nS and nP). Those numbers are floating point for maximum flexibility. A 2S3P bank would consist of 4 batteries. The voltage output would be 2x a unit (24v) and the current output would be 3x a unit. This scaling may be done at the sensor interface and at the display interface. Then the computations – modeling and counting are done with the single battery unit.

## Caution
The voltage sensor is a 3.3v A/D on the PLC to measure 15v. Exceeding 3.3v will blow the A/D and make the monitor mostly useless. It would be difficult to know saturation, a critical sensing element for basic accuracy. A voltage divider is soldered to do this. If more batteries are added in series, then the low voltage leg of the divider will need less resistance. See the 4k7 resistor on the right hand side of the main board diagram at top – feeding A1. It's easy to add a parallel resistor to achieve this whereas the high voltage leg would require removing solder. There is a way to add this resistor to the back of the main PLC board accessed by removing the cover of the device. Remember to rescale and recalibrate the voltage measurement in the monitor application.

## Current Sensor Design
Shunt return a small voltage for a current passing through it. The voltage is small to avoid affecting system performance and generating heat. The voltage is biploar because current may either charge or discharge. So an amplifier is required to generate a high voltage for a 3.3v unipolar A/D that does not change sign. This is easy to do with a single op-amp. See Figure 2. For a shunt that puts out 0.075v at rated current a gain of about 20 is needed. The RC filtering (R1*C106) is performed on the output to also serve as anti-aliasing of op-amp and other circuit noise.

A disadvantage of this design is that 4 A/D are needed for two sensors. Each sensor needs the output voltage and also the common voltage. There is a chip available, TSC2010-IDT, that does differential amplification using three built-in op-amps. The base chip is TSC201. The trailing "0" denotes 20 amplification. There are others: the next size up, "1" is 60. The IDT is the standard quality control for an SOIC-8 surface mount. These sensors use high quality internal resistors and cost about $5.00 each but were not available until 6 months after building the Beta prototype.

## Repository
All information including code, data sheets, scripts, the source for this document is organized in the open GitHub repository https://github.com/davegutz/myStateOfCharge. The MIT license is applied to make all this information open.
Most information is in the primary application folder SOC_Photon, named after the first prototype: a Particle Photon PLC running a 'state of charge' counting algorithm.
Moving alphabetically, the first folder 'Battery State' is a record regarding the theory of LiFeP04 battery state of charge (SOC) monitoring. The subfolder 'EKF' is a record of theory of Extended Kalman Filter as applied to SOC. Inside the 'sandbox' folder are Python models of this topic.
The second folder 'dataReduction' collects raw CoolTerm data capture files '.txt.' The README.md file at the top level has a listing of the different types of scripts run using the 'talk' function through CoolTerm UART transmit/receive interface to generate these files. That is normally done as regression testing to understand code change. Those are sometimes renamed as '.xls', '.xlsx', or '.ods' to plot by hand using Microsoft Excel or Open Document Spreadsheet. By renaming them the hand work is remembered in the repository and not over-written by the next regression test runs through the script series. The '.stc' files are CoolTerm configuration files that are useful to save. The subfolder 'figures' is a permanent collection of data reduction runs, see the 'py' folder of the data reduction Python scripts. The subfolder 'temp' is a scratch folder used by the Python scripts. The '.csv' files in there are useful for debugging the Python scripts.
The folder 'datasheets' has hardware datasheets as well as snapshots of any hand-drawn schematics in 'Schematics' and a folder 'pSpice' with Ltspice modeling of the circuits.
The folder 'lib' is created by VisualStudio Particle Workbench to import Particle-specific code libraries.
The folder 'py' was mentioned before. It is the Python scripts used for data reduction. It was handy to run the same scripts to overlay data on predicted model results. So any design work could be performed by iterating on a particular script run that has a problem, modifying the Python model of the application to find solutions. Inside 'py' is a folder 'pyDAGx' where I store my own Python libraries. The 'venv' folder is maintained by pyCharm IDE.
The folder 'src' has the application source. The app is 'SOC_Photon.ino.' Particle follows the Arduino naming convention. The '.sav' files are my record of a concept that 'tweaked' the charging efficiency to match Coulomb Counting history to incidence of saturation. The concept assumes the current sensors are calibrated perfectly. Inside this folder are 'Adafruit' libraries imported by hand instead of the Particle process, 'hardware' libraries for miscellaneous devices, and 'myLibrary' with my stuff I've accumulated over time – mainly dynamic filters used for application logic.
The folder 'target' is generated by the Particle Workbench to hold application .elf files.
There is a gsheet at https://docs.google.com/spreadsheets/d/19PZ2GmKIlw14doqwePp9xxWH96coLm8WmXdIwlzdxjE/edit#gid=167481175 called 'Truck Camping ALL STUFF' that has a minifest of the prototype hardware. See the tabs 'SOC Device Alpha' and 'SOC Device Beta.' Alpha refers to the Photon design with ADS cards feeding I2C. Beta refers to the Argon design with pure OpAmp devices.
## Design Process Philosopy
For this project I followed a streamlined method that I hope 'self documents.' Data reduction centers on an 'overplot' idea. The run regression, I would overplot the result of old runs on new runs looking for and verifying differences. To run verification, I would overplot the result of new runs on the new model, looking for differences. In verification, there should be a perfect overplot. There are some very rare instances where the data does not overlay perfectly. The presumption is that in achieving a perfect overlay that design meets intent and I avoided a painfully detailed explanation of plot artifacts. Design documentation is done at a higher level with a rough description, not too much detail that would detract from understanding.

## Prototypes
Two situations drove the prototypes and sometimes choice of design.

First, sampling of a low-voltage bipolar current shunt is a the most challenging hardware design in this project. At first I tried to leverage a device described in the literature. It sampled the low voltage using the differential inputs into an A/D converter (ADS1013) sent along an I2C to the Particle devices. It was later improved by adding an op-amp (OPA333) as suggested by Texas Instruments engineers in the datasheets for the ADS1013. This got me started and lives on in the Photon prototypes.

The biggest problem with the initial ADS I2C solution is the throughput. Every call to the I2C device uses between 1 and 100 ms of dead wait time. This sets the throughput for the application. To capture current spikes properly a 0.100 second (100 ms) update time is needed.

Eventually I realized that the Particle devices have plenty of fast A/D converters and that the real challenge was to make a high accuracy bipolar instrumentation amplifier. Microelectronics make a 20:1 chip that matches the 3.3v and 0.075v ranges of the Particle A/D and shunt output range called TSC2010-IDT that is perfect for the task and costs less that $4. It was not available due to COVID pandemic shortatges so instead I used two one-sided A/D converters to manage primary and common voltages of the one-sided OPA333 op-amp circuits to calculate sensed current. This is less accurate but workable since there is plenty of A/D interfaces.

The second situation that drove design is that Particle devices are morphing over time. The Photon is their first / second generation device with Wifi interface and built-in EEPROM to handle power loss. I interfaced to TX/RX UART an HC-06 standard Bluetooth (as opposed to the newer low-energy BLE) for monitoring by the user while moving. When those ran out Particle offers up the third-generation Argon also with Wifi that does not have built-in EEPROM but does have built-in BLE. I bought 47L16 EERAM I2C modules to replace the EEPROM function. This required considerable application programming to support. I tried the BLE function but found that UART terminal apps to support it are poor. So I continued on with the HC-06 since it was a ready solution. The future of Particle is the Photon 2. I would recommend the Photon 2 Development Kit. They are not yet available. It will require the EERAM and HC-06, most likely, unless UART BLE terminals magically appear.

An almost third situtation was software morphing. Particle requires software versions to match hardware devices and those change over time. Fortunately this application is simple enough that basic firmware could handle it and firmware bugs did not affect it. I simply kept up with Particle's releases, always using the most recent as they came out.
## User Interface
I used Serial transmit / receive to communicate with the PLC. Particle provides an API to instantly transmit serial information to the application. There are built-in callback functions ('serialEvent()' and 'serialEvent1()') for the two serial lines that the user populates with whatever commands they want. The user is expected to pair this function with 'Serial.available()' function called within the callback to parse out user input. The callback function excutes each minor frame – call of 'loop().' Particle devices work like Arduino, so calls to 'loop()' happen as fast as the application is able to. The user is responsible for managing time frames.
## Synchronization
I chose to implement a 'loose synchronization' method. Frames are formed by timers called each pass of 'loop().' If time is up for a frame, a boolean is set and any logic associated with the frame is then enables. It becomes 'loose' when events and user input introduce slippage in the frame. I do this for flexibility and to run the application as fast as possible. This application is not time critical. By that there is no feedback control that requires high fidelity dynamic calculation. But I reuse and ecosystem of synchronization used on time critical applications where running as fast as possible is desireable.
The key technology to enable loose synchronization are dynamic digital signal processing algorithms that handle variable update time. My library of functions calculate difference equation coefficients each update for the measured update time.
Dynamic difference equations are aliased – unstable – if they are called too infrequently for the dynamic eigenvalues specified for the algorithm. The library assumes that whatever time slippage occurs is a rare occurence. The user determines the stable update time for each instance and limits the numerical value of update time supplied to the algorithm call to the stable range. This technique limits the destabilizing spikes that occur with coefficients recalculated with unstable update time. The occurence is rare. By the next 'loop()' call, maybe even a few calls, the algorithm has a chance to resume normal operation with a slight glitch.
The glitches tend to be stabilizing, quieting, because update time is less than actual so they are difficult to spot.
Data saved from the application drives the overplot model. The glitches appear in the overplot response in an identical way as in the application so they are impossible to see in a plot.
## Initialization
Dynamic algorithms require a known initial condition for the states. On power-up, the initial first few passes are reserved for sensing the initial conditions and iterating the various 'use-before-calculate' situtations. To speed this up, the application has a 'initialize_all()' function that attempts to perform this in one pass.

The one-wire temperature sensor sometimes requires up to a minute to provide converted values. A special 'reset_temp' flag manages this on power up, extending the initization period until the first good value appears. After initialization, there are rate limits on the converted temperature values to prevent latency from spiking the logic and confusing filters. Fortunately, the battery monitoring algorithms are not very sensitive to temperature changes at the occurence rate they occur.

It is possible to re-initialize on the fly. When the user requests the monitor to be at a different charge state, for some off-line testing of the logic for example, the synchronization ecosystem will turn on the 'reset' flags to force this to happen as on a normal power-up.

A significant simplification is possible for the off line overplot model. The data drives the model and thus must initialize to the same condition to be useful. Rather than develop a separate initialization ecosystem for the model, it simply initializes to the incoming data. The incoming data carries flags names 'reset' or 'reset_temp' that tell the model when to do this. The re-initialization events occur seamlessly too.
## Relibility Concept
There is dual current sense hardware. With flat battery VOC-SOC, current sensing and associated Coulomb Counting integration are critically important to the proper and accurate functioning of this device. This would be true no matter how sophisticated the modeling and filtering employed.

Third current signal constructed using voltage feedback, and EKF and VOC-SOC. The EKF's first function is to solve VOC from SOC. An on-line solver was initially used and replaced by the EKF because the EKF has features that buy it's way on. The EKF has two probability inputs: one is the confidence in the voltage sensor and the second is confidence in the process model SOC. By favoring the SOC (integration of doubly-redundant current a.k.a. Coulomb Counting) the EKF automatically switches and rejects a failed voltage (or bad VOC-SOC curve or bad hysteresis model). If the doubly redundant currents disagree, the EKF can then moderate to isolate the bad current signal. Triplex current sensing is manufactured by system design.

The shunt device and wiring are prime reliable. This is a declaration that the system cannot detect or replace them. However failure is tested and the failure modes are graceful. For example, there is 'quiet' logic that detects disconnected wiring and/or shunt failure and displays a 'conn' status on the OLED.

Note that an important feature of this scheme is annunciation and user intervention. Once the triplex logic isolates a failure it is in a mode where further isolation is not much better than a coin toss. How do you choose between two different wrist watches telling different time? If the user repairs a failure soon after annunciation then exposure to multiple failure scenario is negligible.

Power loss is a normal event. They are caused by user action and by the BMS. To protect LiFeP04 chemistry, the BMS shutsoff charging below 0 C and shutsoff usage below 10v. Features are added to Count Coulombs and monitor faults in presence of normal power loss occurrance.

Except for shutting off, the Battleborn batteries are sensitive to temperature. Accuracy is improved with sensor but not terribly. The most likely consequence of temperature sensor loss would be an unexpected BMS shutoff for low temperature while the device is predicting good time remaining. Temperature sensor failures are monitored and displayed so the user can take action to reduce exposure.

## Real-Time Monitoring
There are three possible ways:
- Connect CoolTerm to the USB
- Connect phone UART terminal to the USB
- Monitor HC-06 standard Bluetooth Serial Output
## Post Process Monitoring
High sample rate is needed to properly bookkeep current integration for spikes. Once that is verified and built in the device build the monitoring process may have as long as 30 minutes between data points. Sensor failures are on the order of 10 seconds between data points. Two circular buffers manage this data collection. Seven points are captured for any critical sensor failure and that buffer frozen until manually reset. It may be downloaded using any of the three monitoring methods. Any and all excess memory is used for the history. The Argon PLCs have some extra EERAM beyond what's needed for sensor failures. And the Argon PLCs have extra PRAM to access as long as the PLC is not depowered. All these are available using any of the three monitoring methods.
## Resistor Quality
The temperature range for this device is about 0C for a heated battery up to about 40C on hot summer day. This is a small swing and 5% resistors would show about 1% effect. And since the battery hysteresis, variation, life and the need to calibrate for installation effects drive accuracy, the resistor quality could be poor. This is unnecessary because the high quality resistors are negligibly more expensive. In the future, 1% 1/4 watt resistors should be procured.

## Cost

## Battery Heating

Figure 2: Current Sensors Functional Circuit Diagram
# Recommendations
1. Procure TSC2010-IDT chips going forward.
2. Procure 1% 1/4 watt resistors going forward.